Connecting a True-Trak 2020™ Monitoring Computer to the Internet

The monitoring computer has one ethernet port.

If the monitoring computer has only one ethernet port it is unlikely that you will be able to use that port to connect to the internet and the FasTrak2™ board at the same time. The FasTrak2™ board uses a fixed IP address, usually 192.168.254.99, and unless the network that you are going to connect to uses the same first three octets, 192.168.254, and unless no one else on the network is using the same last octet, 99, then connecting using this port will be very difficult.

I would suggest getting a second ethernet card or usb ethernet interface and using that port to connect to the internet.

The monitoring computer has two ethernet ports.

If the monitoring computer has two ethernet ports then one will be used to connect to the FasTrak2™ board. The other ethernet port will be:

1. Unused
If this is the case you can probably just plug the second port into a network hub and it will connect automatically.
2. Connected to a local network used only for the True-Trak 2020™ computers.

3. Connected to the company network.

If you have no internet connection already you need to contact your system administrator to have it enabled for the time that you need it.

If the port is